## Slide 1: Design, Fabrication, and Testing of a Capsule With Hybrid Locomotion for Gastrointestinal Tract Exploration
Alexandru Vasile, Manuel Ojeda

## Slide 2: Magnetic System
Provides external active locomotion in partially collapsed or uncollapsed regions
Characteristics of external magnet: 1.5 kg, 1.21 T, cylindrical shape (diameter=60mm, length=70mm)

## Slide 3: On-Board Electronics
Four-layer circular electronic board (diameter = 10.3 mm, thickness = 2.5 mm)
Deep sleep modality was also implemented
A single rechargeable lithium-ion polymer battery as energy source
Battery is in the range of 18h to 25min, depending on the legged mechanism (180° leg movement consumes 12 min of autonomy)

## Slide 4: On-Board Electronics
Human-machine interface is compatible with voice commands
Texas Instruments microcontrollers effective for LGI tract telemetry

## Slide 5: Packaging and Assembly
Chassis and body fabricated in Ergal (aluminum alloy)
Cylindrical tank fabricated in polyarylether ether ketone (polymer PEEK)
Composed of 60 different parts
Assembled measures 14mm diameter, 44mm length, weights 13.5g

## Slide 6: Experimental Validation
Legs pulled the cables and an average force of 3.58N

## Slide 7: Experimental Validation
Implemented preliminary in vitro, ex vivo, in vivo trials for time estimation
In vitro: 20cm tract of latex colon simulator (Kyoto Kagaku)
Ex vivo: 20cm fresh porcine colon segment
In vivo: 4 female pigs with a weight 25-35 kg
The capsule was observed by a gastroscope

## Slide 8: Experimental Validation
The magnetic field can move and steer the capsule in collapsed regions
The legged mechanism can lift and distend collapsed regions
In vitro, the test took within 10 min and Ex vivo took in 7 cases was within 10 min
In six cases, out of ten, the capsule covered the 40 cm in an average of 5 min.
Notes: The three failed trials were mainly due to the absence of muscular tone

## Slide 9: Conclusion
Two different solutions for active locomotion merged successfully
Comparison with other locomotion modules is power consumption and speed
Previous prototypes: 4-leg capsule 3 cm/min, 8-leg capsule 4 cm/min, 12-leg capsule 5 cm/min, hybrid capsule 8 cm/min

## Slide 10: Future work
Miniaturized mechanism
New leg shapes to minimize local tissue stresses
Real-time wireless vision module, not commercially available at the moment of experiments
Developing a 20fps real-time wireless camera system for capsule endoscopy